Networked Fast Clock Master
Instruction Manual

MRB-FCM v1.0 Wired and Wireless

Basic Installation - Wiring

Write stuff here

Advanced User Information

- Packet format
- EEPROM configuration addresses
Screen 1.0: Main Screen – Real Time Clock Mode

        AM
        REAL
FC:1200A 11 Nov 2012
FAST CONF
12:34
Element	Description
12:34	The current real time, in hour/minute form. If 24 hour real time is selected, this will display with the leading zero. If 12 hour real time is selected, the leading zero will be suppressed.
11 Nov 2012	The current real day, month, and year.
FC:1200A	The current state of the fast clock. This will display FC: if the clock will immediately resume counting upon entry into Fast Clock Mode(FCM), and FH: if the clock will go into hold upon entering FCM.
AM	If 24 hour real time is selected, this will show “24”. In 12 hour real time mode, this will show AM or PM as appropriate.
REAL	An indicator that the clock is currently in Real Time Mode (RTM).
FAST	Soft key 1 will enter into Fast Clock Mode – see Screen 1.1
CONF	Soft key 4 will enter the Configuration Menu – see Screen 2.0

Screen 1.1: Main Screen – Fast Clock Mode

        AM
        FAST
 12.5:1 12:34:56AM
REAL HOLD RST CONF
12:34
Element	Description
12:34	The current fast time, in hour/minute form. If 24 hour fast time is selected, this will display with the leading zero. If 12 hour fast time is selected, the leading zero will be suppressed. In hold mode, the display will show “HOLD”
12:34:56AM	The current real time, in hours/minutes/seconds and an AM/PM indicator if the real time clock is set up for 12 hour mode.
12.5:1	The current fast time ratio, expressed in units of fast time that will pass during 1 unit of real time. (eg, 12.5 seconds will elapse for every real second in this example.)
REAL	Soft key 1 will enter into Real Time Clock Mode – see Screen 1.0
HOLD	Soft key 2 will toggle between the fast clock time advancing at the programmed ratio and the fast clock being paused - “hold” mode. If the clock is running, it will display “HOLD”, and if the clock is paused, it will display “RUN”, reflecting the mode it will toggle into.
RST	Soft key 3 will reset the fast clock to the configured start time. See screen 1.2 for the reset confirmation screen, and see screen 2.7 for configuring the fast clock start time.
CONF	Soft key 4 will enter the Configuration Menu – see screen 2.0a

Screen 1.2: Fast Clock Reset Confirmation

   !! CONFIRM !!
  Reset Fast Clock
to Which Start Time?
0800 1200 1800 CNCL
Element	Description
0800	Soft key 1 will reset the fast clock time to the first configured starting time (see screen 2.7) and return to the Fast Clock Mode main screen (screen 1.1). The time displayed will always be in 24h format so that it fits above the button.
1200	Soft key 3 will reset the fast clock time to the second configured starting time (see screen 2.7) and return to the Fast Clock Mode main screen (screen 1.1). The time displayed will always be in 24h format so that it fits above the button.
1800	Soft key 3 will reset the fast clock time to the third configured starting time (see screen 2.7) and return to the Fast Clock Mode main screen (screen 1.1). The time displayed will always be in 24h format so that it fits above the button.
CNCL	Soft key 4 will return to the Fast Clock Mode main screen (screen 1.1) without affecting the current fast time.

Screen 2.0a: Main Configuration Menu Screen 1

> Real 12/24
  Real Time
  Real Date
 UP DOWN SLCT BACK
Element	Description
>	A cursor indicating the current menu selection
Real 12/24	Configure real time to be in 12 or 24 hour mode – see screen 2.1
Real Time	Set current real time – see screen 2.2
Real Date	Set current real date – see screen 2.4
UP	Soft key 1 – will move the cursor up the menu structure. Soft key will be disabled if at the top of the configuration menu list.
DOWN	Soft key 2 – will move the cursor down the menu structure. If the cursor is moved past the bottom of the displayed list, the configuration menu will progress to the second configu screen 2.0b.
SLCT	Soft key 3 – will select the current configuration option.
BACK	Soft key 4 – will return to the main screen in either real time clock mode (screen 1.0) or fast clock mode (screen 1.1), depending on which was used to enter the configuration menu.

Screen 2.0b: Main Configuration Menu Screen 2

> Fast 12/24
  Fast Ratio
  Fast Start Hold
 UP DOWN SLCT BACK
Element	Description
>	A cursor indicating the current menu selection
Fast 12/24	Configure fast time to be in 12 or 24 hour mode – see screen 2.6
Fast Ratio	Set fast clock ratio of fast time to real elapsed time – see screen 2.7
Fast Start Hold	Configure if the fast clock will always be set to “hold” when fast clock mode is entered – see screen 2.11
UP	Soft key 1 – will move the cursor up the menu structure. If the cursor is moved up beyond the top of the list, it will go back to configuration screen 2.0a.
DOWN	Soft key 2 – will move the cursor down the menu structure. If it passes the bottom of the displayed list, the configuration menu will progress to screen 2.0c.
SLCT	Soft key 3 – will select the current configuration option.
BACK	Soft key 4 – will return to the main screen in either real time clock mode (screen 1.0) or fast clock mode (screen 1.1), depending on which was used to enter the configuration menu.

Screen 2.0c: Main Configuration Menu Screen 3

> Fast Start Time 1
  Fast Start Time 2
  Fast Start Time 3
 UP DOWN SLCT BACK
Element	Description
>	A cursor indicating the current menu selection
Fast Start Time 1	Set the first start time at which the fast clock can be reset to – typically whatever hour/minute of the fast day your operating session will start on. Fast Start Time 1 is what the clock will default to using when first powered up. See screen 2.9 for time setup. Will appear on soft key 1 when a reset is requested (screen 1.2).
Fast Start Time 2	Set the second start time at which the fast clock can be reset to – typically whatever hour/minute of the fast day your operating session will start on. See screen 2.9 for time setup. Will appear on soft key 2 when a reset is requested (screen 1.2).
Fast Start Time 3	Set the third start time at which the fast clock can be reset to – typically whatever hour/minute of the fast day your operating session will start on. See screen 2.9 for time setup. Will appear on soft key 3 when a reset is requested (screen 1.2).
UP	Soft key 1 – will move the cursor up the menu structure. If the cursor is moved up beyond the top of the list, it will go back to configuration screen 2.0b.
DOWN	Soft key 2 – will move the cursor down the menu structure. If it passes the bottom of the displayed list, the configuration menu will progress to screen 2.0d.
SLCT	Soft key 3 – will select the current configuration option.
BACK	Soft key 4 – will return to the main screen in either real time clock mode (screen 1.0) or fast clock mode (screen 1.1), depending on which was used to enter the configuration menu.

Screen 2.0d: Main Configuration Menu Screen 4

> Time Pkt Interval
  Node Address
  TH Address
 UP DOWN SLCT BACK
Element	Description
>	A cursor indicating the current menu selection
Time Pkt Interval	Configure how often the master clock will send synchronization packets to slave clocks. See screen 2.12
Node Address	Configure the MRBus address of the fast clock master. See screen 2.14
TH Address	Configure the address of a MRBW-TH temperature/humidity sensor. See screen 2.17
UP	Soft key 1 – will move the cursor up the menu structure. If the cursor is moved up beyond the top of the list, it will go back to configuration screen 2.0c.
DOWN	Soft key 2 – will move the cursor down the menu structure. If on the last item, the soft key will be disabled.
SLCT	Soft key 3 – will select the current configuration option.
BACK	Soft key 4 – will return to the main screen in either real time clock mode (screen 1.0) or fast clock mode (screen 1.1), depending on which was used to enter the configuration menu.

Screen 2.0e: Main Configuration Menu Screen 5

> TH Timeout
  Temperature Units
  Diagnostics
 UP DOWN SLCT BACK
Element	Description
>	A cursor indicating the current menu selection
TH Timeout	Configure the maximum time between two MRBW-TH packets before the sensor is considered to have “timed out”. See screen 2.19
Temperature Units	Configure which unit s (degrees Fahrenheit or Celsius) that temperatures from an MRBW-TH will be displayed in. See screen 2.21
Diagnostics	View diagnostic information about the fast clock master node – see screen 2.16.
UP	Soft key 1 – will move the cursor up the menu structure. If the cursor is moved up beyond the top of the list, it will go back to configuration screen 2.0c.
DOWN	Soft key 2 – will move the cursor down the menu structure. If on the last item, the soft key will be disabled.
SLCT	Soft key 3 – will select the current configuration option.
BACK	Soft key 4 – will return to the main screen in either real time clock mode (screen 1.0) or fast clock mode (screen 1.1), depending on which was used to enter the configuration menu.

Screen 2.1: Real Time 12/24h Configuration Screen

Real Time 12/24H:
[*] 12H (AM/PM)
[ ] 24H (0000h)
12hr 24hr SAVE CNCL
Element	Description
*	A cursor indicating the current selection
12H (AM/PM)	Configure real time to be displayed in 12 hour, AM/PM time.
24H (0000h)	Configure real time to be displayed in 24 hour time.
12hr	Soft key 1 – selects 12 hour time.
24hr	Soft key 2 – selects 24 hour time.
SAVE	Soft key 3 – saves real time format selection and returns to configuration screen 2.0a.
CNCL	Soft key 4 – returns to configuration screen 2.0a without saving real time format change.

Screen 2.2: Real Time Set Screen

Current Real Time:
12:34:56 AM
^^
 ++ -- >> GO
Element	Description
12:34:56	The current real time, displayed as 12 or 24 hour time as selected in screen 2.1. (In 24h time, the AM/PM indicator will not display. In 12h mode, AM/PM cannot be directly adjusted, but advancing the hours over midnight or noon will cause the transition.)
^^	A cursor indicating which part of real time is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the time.
--	Soft key 2 – decrements the currently selected part of the time.
>>	Soft key 3 – moves the cursor to the next component of time to the right (hours move to minutes move to seconds, which then wraps around to hours)
GO	Soft key 4 – advances to screen 2.3 which confirms the time being set.

Screen 2.3: Real Time Set Confirmation Screen

Current Real Time:
12:34:56 AM

BACK SAVE CNCL
Element	Description
12:34:56	The current real time to be set as configured in screen 2.2, displayed as 12 or 24 hour time as selected in screen 2.1. (In 24h time, the AM/PM indicator will not display.)
BACK	Soft key 1 – returns to screen 2.2, so that the real time to be set can be changed.
SAVE	Soft key 3 – saves the displayed real time to the internal real time clock.
CNCL	Soft key 4 – cancels changing the real time and returns to the main configuration menu (screen 2.0a).

Screen 2.4: Real Date Configuration Screen

Current Real Date:
11 Nov 2012
^^
 ++ -- >> GO
Element	Description
^^	A cursor indicating which part of real time clock date is subject to adjustment by soft keys 1 and 2.
11 Nov 2012	The current real date
++	Soft key 1 – increments the currently selected part of the date.
--	Soft key 2 – decrements the currently selected part of the date.
>>	Soft key 3 – moves the cursor to the next component of date to the right (day moves to month moves to year, which then wraps around to day)
GO	Soft key 4 – advances to screen 2.5 which confirms the real time clock date being set.

Screen 2.5: Real Date Confirmation Screen

Current Real Date:
11 Nov 2012

BACK SAVE CNCL
Element	Description
11 Nov 2012	The current date, as selected in screen 2.4
BACK	Soft key 1 – returns to screen 2.4, so that the date to be set can be changed.
SAVE	Soft key 3 – saves the displayed date to onboard real time clock
CNCL	Soft key 4 – cancels changing the date and returns to the main configuration menu (screen 2.0a).

Screen 2.6: Fast Time 12/24h Configuration Screen

Fast Time 12/24H:
[*] 12H (AM/PM)
[ ] 24H (0000h)
12hr 24hr SAVE CNCL
Element	Description
*	A cursor indicating the current selection
12H (AM/PM)	Configure fast time to be displayed in 12 hour, AM/PM time.
24H (0000h)	Configure fast time to be displayed in 24 hour time.
12hr	Soft key 1 – selects 12 hour time.
24hr	Soft key 2 – selects 24 hour time.
SAVE	Soft key 3 – saves fast time format selection and returns to configuration screen 2.0b.
CNCL	Soft key 4 – returns to configuration screen 2.0b without saving fast time format change.

Screen 2.7: Fast Clock Ratio Configuration Screen

Fast Clock Ratio:
12.5:1
^^
 ++ -- >> GO
Element	Description
12.5:1	The ratio between how quickly fast time passes and how quickly real time passes. As an example, 4.0:1 would yield the passage of 24 hours of fast time in 6 hours.
^^	A cursor indicating which part of the ratio is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the ratio.
--	Soft key 2 – decrements the currently selected part of the ratio.
>>	Soft key 3 – moves the cursor to the next component of the ratio to the right (integer portion or tenths), or wraps around if already on tenths.
GO	Soft key 4 – advances to screen 2.8 which confirms the ratio being set

Screen 2.8: Fast Clock Ratio Confirmation Screen

Fast Clock Ratio:
12.5:1

BACK SAVE CNCL
Element	Description
12.5:1	The ratio between fast time and real time as selected in screen 2.7.
BACK	Soft key 1 – returns to screen 2.7, so that the fast clock ratio to be set can be changed.
SAVE	Soft key 3 – saves the displayed fast clock ratio to configuration memory
CNCL	Soft key 4 – cancels changing the fast clock ratio and returns to the main configuration menu (screen 2.0b).

Screen 2.9: Fast Start Time Set Screen

Fast Start Time X:
12:34:56 AM
^^
 ++ -- >> GO
Element	Description
Fast Start Time X:	X will be 1, 2, or 3, corresponding to which fast clock starting time is being set. See screen 1.2 for where fast clock start times can be selected during a reset, and screen 2.0c for how each start time configuration is reached.
12:34:56	The desired start time for the fast clock, displayed as 12 or 24 hour time as selected in screen 2.6. (In 24h time, the AM/PM indicator will not display. In 12h mode, AM/PM cannot be directly adjusted, but advancing the hours over midnight or noon will cause the transition.)
^^	A cursor indicating which part of fast start time is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the time.
--	Soft key 2 – decrements the currently selected part of the time.
>>	Soft key 3 – moves the cursor to the next component of time to the right (hours move to minutes move to seconds, which then wraps around to hours)
GO	Soft key 4 – advances to screen 2.10 which confirms the fast start time being set.

Screen 2.10: Fast Start Time Confirmation Screen

Fast Start Time X:
12:34:56 AM

BACK SAVE CNCL
Element	Description
Fast Start Time X:	X will be 1, 2, or 3, corresponding to which fast clock starting time is being set. See screen 1.2 for where fast clock start times can be selected during a reset, and screen 2.0c for how each start time configuration is reached.
12:34:56	The fast clock start time to be set as configured in screen 2.6, displayed as 12 or 24 hour time as selected in screen 2.6. (In 24h time, the AM/PM indicator will not display.)
BACK	Soft key 1 – returns to screen 2.9, so that the fast clock start time to be set can be changed.
SAVE	Soft key 3 – saves the displayed fast clock start time to configuration memory
CNCL	Soft key 4 – cancels changing the fast clock start time and returns to the main configuration menu (screen 2.0b).

Screen 2.11: Fast Clock Hold Configuration Screen

Fast Start Mode:
[*] RUN (12:34A)
[ ] HOLD
RUN HOLD SAVE CNCL
Element	Description
*	A cursor indicating the current selection
[ ] RUN	Configure fast time to start counting immediately when fast clock mode is entered. As a convenience, the configured fast clock starting time is shown after “Run”.
[ ] HOLD	Configure fast time to immediately go to “hold” when fast clock mode is entered.
RUN	Soft key 1 – selects run mode.
HOLD	Soft key 2 – selects hold mode.
SAVE	Soft key 3 – saves fast time run/hold mode selection and returns to configuration screen 2.0c.
CNCL	Soft key 4 – returns to configuration screen 2.0c without saving fast time run/hold mode change.

Screen 2.12: Time Packet Interval Configuration Screen

Time Pkt Interval:
001.2 sec
^
 ++ -- >> GO
Element	Description
001.2 sec	The desired time between broadcasting time packets on the network, expressed in seconds. For most applications, 1-3 seconds is probably optimal (meaning a setting of 1.0-3.0).
^^	A cursor indicating which digit of the time is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the time.
--	Soft key 2 – decrements the currently selected part of the time.
>>	Soft key 3 – moves the cursor to the next component of time to the right, or will wrap back around if already on the rightmost digit
GO	Soft key 4 – advances to screen 2.13 which confirms the packet interval time being set.

Screen 2.13: Time Packet Interval Confirmation Screen

Time Pkt Interval:
001.2 sec

BACK SAVE CNCL
Element	Description
001.2 sec	The desired time between broadcasting time packets on the network, expressed in seconds. For most applications, 1-3 seconds is probably optimal (meaning a setting of 1.0-3.0).
BACK	Soft key 1 – returns to screen 2.12, so that the fast clock start time to be set can be changed.
SAVE	Soft key 3 – saves the displayed fast clock start time to configuration memory and returns to the main configuration menu (screen 2.0c)
CNCL	Soft key 4 – cancels changing the fast clock start time and returns to the main configuration menu (screen 2.0c).

Screen 2.14: Fast Clock Master Node Address Configuration Screen

Fast Clock Addr:
0x1A
  ^
 ++ -- >> GO
Element	Description
0x1A	The hexadecimal network address of the fast clock master node. All MRBus nodes must have a unique address. For pure fast clock applications, changing this should not be needed.
^^	A cursor indicating which digit of the address is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the address.
--	Soft key 2 – decrements the currently selected part of the address.
>>	Soft key 3 – moves the cursor to the next digit of address to the right
GO	Soft key 4 – advances to screen 2.15 which confirms the network address.

Screen 2.15: Fast Clock Master Node Address Confirmation Screen

Fast Clock Addr:
0x1A

BACK SAVE CNCL
Element	Description
0x1A	The hexadecimal network address of the fast clock master node to be set.
BACK	Soft key 1 – returns to screen 2.14, so that the node address to be set can be changed.
SAVE	Soft key 3 – saves the displayed fast clock node address to configuration memory and returns to the main configuration menu (screen 2.0c)
CNCL	Soft key 4 – cancels changing the fast clock node address and returns to the main configuration menu (screen 2.0c).

Screen 2.16: Diagnostics Screen

Diagnostics: 122kl/s
Bus:11.6V Addr:0x1A
TH : 3.1V
RFSH BACK
Element	Description
Bus:11.6V	The current power supply voltage for the fast clock master node. Will read roughly 0.5V lower than the actual bus voltage, as the sensing is done after the protection diode on the front end.
Addr:0x1A	The MRBus network address of the fast clock master node.
122kl/s	The speed at which the main loop is executing, in thousands of loops per second. This is almost meaningless to an end user, but is handy for debugging slow reponse problems.
TH : 3.2V	If a MRBW-TH temperature/humidity monitor is configured and the fast clock has received a packet within the timout period, the supply voltage for the MRBW-TH will be displayed here. This is useful for checking the battery voltage on wireless, battery powered temperature/humidity nodes.
RFSH	Soft key 1 – Forces immediate refresh of the values displayed on the diagnostics screen. The screen will refresh itself every second on its own.
CNCL	Soft key 4 – cancels out of diagnostic mode and returns to the main configuration menu (screen 2.0e).

Screen 2.17: Temperature/Humidity Node Address Configuration Screen

Temp/Humidity Addr:
0x20
  ^
 ++ -- >> GO
Element	Description
0x20	The MRBus address of the MRBW-TH node to be monitored. Setting this to 0x00 will cause the display to show “”T/H Off” and disable any display of temperature and humidity.
^	A cursor indicating which digit of the address is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the address.
--	Soft key 2 – decrements the currently selected part of the address.
>>	Soft key 3 – moves the cursor to the next component of time to the right, or will wrap back around if already on the rightmost digit
GO	Soft key 4 – advances to screen 2.18 which confirms the TH address to be monitored.

Screen 2.18: Temperature/Humidity Node Address Confirmation Screen

Temp/Humidity Addr:
0x20

BACK SAVE CNCL
Element	Description
0x20	The MRBus address of the MRBW-TH node to be monitored. Setting this to 0x00 will cause the display to show “”T/H Off” and disable any display of temperature and humidity.
BACK	Soft key 1 – returns to screen 2.17, so that the MRBW-TH source address can be changed.
SAVE	Soft key 3 – saves the displayed temperature/humidity source address to configuration memory and returns to the main configuration menu (screen 2.0d)
CNCL	Soft key 4 – cancels changing the temperature/humidity source address and returns to the main configuration menu (screen 2.0d).

Screen 2.19: Temperature/Humidity Timeout Configuration Screen

Temp/Hum Timeout:
0012 sec
^
 ++ -- >> GO
Element	Description
0012 sec	The maximum amount of allowed time between received packets from the configured MRBW-TH node. If a valid 'S' packet from the TH node is not configured within this interval, the fast clock will stop displaying temperature/humidity until another packet is received.
^	A cursor indicating which digit of the time is subject to adjustment by soft keys 1 and 2.
++	Soft key 1 – increments the currently selected part of the time.
--	Soft key 2 – decrements the currently selected part of the time.
>>	Soft key 3 – moves the cursor to the next component of time to the right, or will wrap back around if already on the rightmost digit
GO	Soft key 4 – advances to screen 2.20 which confirms the timeout being set.

Screen 2.20: Temperature/Humidity Timeout Confirmation Screen

Temp/Hum Timeout:
0012 sec

BACK SAVE CNCL
Element	Description
0012 sec	The maximum amount of allowed time between received packets from the configured MRBW-TH node. If a valid 'S' packet from the TH node is not configured within this interval, the fast clock will stop displaying temperature/humidity until another packet is received.
BACK	Soft key 1 – returns to screen 2.19, so that the temperature/humidity packet time to be set can be changed.
SAVE	Soft key 3 – saves the displayed temperature/humidity timeout to configuration memory and returns to the main configuration menu (screen 2.0e)
CNCL	Soft key 4 – cancels changing the temperature/humidity timeout and returns to the main configuration menu (screen 2.0e).

Screen 2.21: Temperature Units Configuration Screen

Temperature Units:
[*] Degrees F
[ ] Degrees C
 F C SAVE CNCL
Element	Description
*	A cursor indicating the current selection
Degrees F	Configure temperature to be displayed in degrees Fahrenheit
Degrees C	Configure temperature to be displayed in degrees Celsius
F	Soft key 1 – selects degrees Fahrenheit
C	Soft key 2 – selects degrees Celsius
SAVE	Soft key 3 – saves real time format selection and returns to configuration screen 2.0e.
CNCL	Soft key 4 – returns to configuration screen 2.0e without saving real time format change.